## Slide 1
Angawatch: Kenya's First Cognitive Community
Yatta Plateau, Machakos County · Power the Community 2026
1.17°S, 37.45°E · Submission Deadline: April 15, 2026 · energymentors.org/participate
gitahi.githinji@strathmore.edu
ANGAWATCH ECO-COMMUNITY
1

## Slide 2
[INSERT IMAGE: Kenyan nurse at community health centre — rural setting]
Meet Wanjiku — she built Kenya's healthcare system
KES 84,230 net
Registered Nurse, 8 years experience, Yatta sub-county
KES 110,000 gross combined with teacher husband Kamau
Net income KES 84,230 after PAYE, NHIF, NSSF
Two school-age children · elderly parent visits monthly
2

## Slide 3
Her basics cost KES 36,100 before food, school, or savings
KES 36,100/month
Rent (3-room Matuu): KES 18,000 — nothing owned after 25 years
Electricity (KPLC prepaid): KES 7,200 — 15–25 outages/year
Commute (boda + matatu): KES 6,600 — 2+ hours daily each way
Cooking (retail LPG): KES 1,560 — KES 1,300–1,500 per cylinder
[ Visual / Chart ]
3

## Slide 4
[INSERT IMAGE: Cost comparison infographic — Off-Grid vs Grid-Interactive architecture]
Full off-grid costs 4× more — Wanjiku cannot pay that
+KES 1.5B
True off-grid for 2,000 families: needs 14,400 kWh BESS (4× our design)
Additional cost: +KES 1,500M above grid-interactive design
Adds ~KES 8,300 to every family's monthly mortgage — unaffordable
Engineering purity that prices out the people it claims to serve
4

## Slide 5
Can a nurse afford an energy system designed for her?
KES 9/kWh
Not designed for a utility engineer — designed for Wanjiku
Electricity bill: KES 7,200 → KES 930/month (87% reduction)
Reliability: 75% uptime → 99.6% (BESS + genset + KPLC backup)
Answer: Yes — if we build houses around solar, not the reverse
5

## Slide 6
We don't retrofit solar onto houses — we build houses around solar
35% cheaper
CSEB from Yatta volcanic laterite → 35% below concrete block cost
Passive cooling eliminates air conditioning → zero cooling load
Roof orientation optimised for solar before architectural drawings
Community scale unlocks institutional pricing for all components
6

## Slide 7
Three decisions deliver 80% of all resident benefit
80%
[chart_07_bcr_comparison.html — Three decisions BCR comparison]
Decision 1: Biogas + LPG SACCO → PM2.5 eliminated, KES 1,200–2,700 cooking saving (BCR 2.8)
Decision 2: CSEB construction → 35% cost saving, zero cooling load, zero AC bill forever
Decision 3: M-Pesa SmartMeter KES 9/kWh → 64% electricity saving (BCR 2,304)
7

## Slide 8
A
What Angawatch Is — And What It Deliberately Is Not
IS: A grid-interactive microgrid with islanding capability
IS: An affordability-first community for KES 84,230-net families
IS NOT: An off-grid vanity project — Wanjiku cannot pay 4× the BESS
IS NOT: A retrofit — every wire laid before the first brick is placed
8

## Slide 9
Yatta Plateau: 102 hectares chosen with precision
60km from Nairobi
1.17°S, 37.45°E · near Matuu, Yatta Sub-County, Machakos County
102 hectares (252 acres) at 1,450–1,550m above sea level
60km from Nairobi via A109; SGR Athi River station 25km
Existing 33kV substation Matuu 4km — grid connection KES 36M
[ Visual / Chart ]
9

## Slide 10
Six site advantages — no compromises made
5.18 kWh/m²/day
Solar: 5.18 kWh/m²/day average (PVGIS v5.2 verified) — best within 80km of Nairobi
Elevation 1,450–1,550m ASL — passive cooling, 17–27°C year-round, zero AC
Yatta Canal 2km — gravity irrigation (unsuitable for power — too weak)
Basaltic laterite: CSEB-grade, 5% cement binder, KS 02-1070 compliant
33kV Matuu substation 4km — cheapest grid connection in region
A109 highway — direct link to Nairobi and Machakos town
[ Visual / Chart ]
10

## Slide 11
Eight zones — every hectare of 102ha is purposeful
102 ha
Residential: 37ha (36%) — 2,000 units, hybrid tenure model
YattaFarm + chrysanthemum: 20ha (22%) — food cooperative + export flowers
Community Hub (CHC, schools, worship, recreation): 12ha (13%)
Jua Kali industrial zone: 8ha (9%) — workshops, CSEB factory, EV depot
Energy infrastructure: 3ha — 4 energy hubs, biogas plant, stormwater pond
Roads, green space, commercial strip: remaining 22ha
[ Visual / Chart ]
11

## Slide 12
Three archetypes — every income bracket deliberately served
KES 38K–160K/mo
Wanjiku + Kamau (Nurse + Teacher): KES 110K gross → 2BR/3BR KMRC mortgage
Hassan (Boda Boda operator): KES 38K net → 1BR cooperative rental, EV boda savings
Deputy Principal: KES 160K combined → 4BR, DTI 41.2%, no AHP subsidy needed
All three archetypes drawn from KNBS 2019 Census + NCK + TSC salary data
[ Visual / Chart ]
12

## Slide 13
2,000 units — this exact mix for one exact reason
1,130 × 2BR
150 × 1BR (42m²): cooperative rental KES 10,000–12,000/month — Hassan's entry point
1,130 × 2BR (75m²): KMRC mortgage KES 33,015/month — sweet spot for KES 110K household
700 × 3BR (93m²): KMRC mortgage KES 40,803/month — Wanjiku's family home
20 × 4BR (115m²): KES 48,615/month — Deputy Principal professional cohort
[ Visual / Chart ]
13

## Slide 14
A KMRC mortgage builds wealth — renting builds nothing
25 years
KMRC 8.99% p.a., 25-year term — longest affordable finance in Kenya
2BR at KES 33,015/month builds full title deed after 300 payments
Renting KES 18,000/month × 25 years = KES 5.4M paid, zero equity
Yatta Plateau land appreciates as A109 corridor infrastructure improves
[ Visual / Chart ]
14

## Slide 15
Angawatch saves each family KES 37,993 per month vs Nairobi
KES 37,993 saved
[chart_04_household_cost.html — Grouped bar: Angawatch vs Nairobi by cost category]
Angawatch total (3BR family): KES 48,107/month including EMI + all utilities
Equivalent Nairobi satellite: KES 86,100/month — renting, not owning
Annual saving: KES 455,916 per year compounding toward financial security
15

## Slide 16
Twenty Ekeja clusters — neighbourhood design rooted in Maa tradition
20 clusters
20 Ekeja clusters × 64–100 units = 2,000 homes in walkable neighbourhoods
Each cluster: shared courtyard, borehole access, laundry court, food forest
Social design: neighbours know neighbours — crime prevention by design
Courtyard = energy hub + EV carport + communal solar carport canopy
[ Visual / Chart ]
16

## Slide 17
Yatta laterite makes better blocks than concrete — for 35% less
35% cheaper
Yatta volcanic laterite: only 5% cement binder (vs 8–10% standard CSEB)
KS 02-1070 certified — full Kenya Standards compliance
Build cost KES 46,500/m² VAT-inclusive vs ~KES 60,000/m² conventional
Community labour during construction: local jobs + skills transfer
[ Visual / Chart ]
17

## Slide 18
From approval to full community in four years
2028 first occupancy
2026–27: Planning approvals, land allocation, DFI financial close
Mid-2028: First occupancy — Phase 1 (500 units, energy systems online)
2029: Phase 2 complete — 1,500 units, YattaFarm fully operational
2030: Full community — all 2,000 units, all systems active, all revenue lines running
[ Visual / Chart ]
18

## Slide 19
5,734 MWh generated · 4,355 consumed · 1,379 exported
1,379 MWh exported
[chart_01_energy_balance.html — Stacked bar: Generation vs Demand sectors + Export]
Solar: 5,479.85 MWh/year (SMA Sunny Design validated April 7, 2026)
Biogas: 254 MWh/year (40-cow dairy + community waste → 773 m³/day)
Community demand: 4,355 MWh/year across 10 sectors (8% loss factor)
Export: 1,379 MWh × KES 12/kWh = KES 16.5M/year net metering income
19

## Slide 20
7,680 Jinko Tiger Neo bifacial panels — 3,360 kWp effective
3,360 kWp
7,680 × Jinko JKM425N-54HL4R-BDB Tiger Neo N-Type Bifacial 425W panels
Nameplate 3,264 kWp; effective 3,360 kWp with 3% bifacial rear-ground gain
Performance Ratio 0.82 — conservative Sunny Design standard
Array tilt and azimuth optimised for 1.17°S equatorial sun path
[ Visual / Chart ]
20

## Slide 21
✓
SMA Sunny Design Validates 5,479.85 MWh/year — April 7, 2026
Professional simulation: Nairobi met station 71km, PVGIS v5.2 data
PR 0.82 standard · 3,360 kWp effective DC · bifacial correction applied
Previous hand calculation: 5,515 MWh — only 0.6% difference. Design confirmed.
Full Sunny Design report included as Appendix B of submission document
21

## Slide 22
3,600 kWh CATL LFP battery — 99.6% community uptime
99.6% uptime
18 × CATL EnerOne 200kWh LFP modules = 3,600 kWh installed capacity
3,240 kWh usable at 90% DoD — exceeds 3,027 kWh night requirement by 7%
Cummins C220N5 genset (biogas-fuelled) provides additional backup layer
Year 17 full replacement — fully costed in financial model (LFP cycle life)
[ Visual / Chart ]
22

## Slide 23
773 m³/day biogas — from 40-cow dairy plus community waste
254 MWh/year
40-cow commercial dairy: largest single biogas input source on site
Community organic waste provides additional continuous feedstock
Total usable biogas: 773 m³/day (234 to cooking, 539 to genset)
539 m³/day to Cummins C220N5 genset = 254 MWh/year electricity
[ Visual / Chart ]
23

## Slide 24
Biogas to schools and clinics — not homes. The honest decision.
3,200 m³/day needed
Cooking for 2,000 families needs 3,200 m³/day — we produce only 773 m³/day
Spreading thin biogas to 2,000 homes achieves nothing meaningful for anyone
CHC + 2 schools + market kitchen: biogas eliminates PM2.5 for 400 children daily
Homes use SACCO bulk LPG (Phase 1) → solar induction cooking (Phase 3, Year 10+)
[ Visual / Chart ]
24

## Slide 25
Three-phase cooking strategy saves KES 100M in CAPEX
KES 100M saved
Phase 1: SACCO bulk LPG for all homes — immediate charcoal replacement, Day 1
Phase 2: Biogas to CHC, 2 schools, market — PM2.5 eliminated at institutions
Phase 3 (Year 10+): Solar induction for homes as generation surplus grows
Full induction from Day 1 = +KES 100M CAPEX + 3× solar capacity — unviable
[ Visual / Chart ]
25

## Slide 26
KES 9/kWh via *384# — the Kenyan innovation no other team can replicate
KES 9/kWh
USSD code *384# on any Safaricom line — no smartphone or data connection needed
Purchase tokens in any amount, at any time — no minimum unit purchase barrier
Net metering credits automatically deposited to M-Pesa wallet monthly
KES 2.5M software development → BCR 2,304 (KES 5.76B lifetime family saving)
[ Visual / Chart ]
26

## Slide 27
July dispatch: solar peaks at 2,600kW noon, exports 800kW to grid
2,600 kW peak
[24-hour power flow chart for July — solar, BESS, genset, demand, export by hour]
5am–8am: Cummins genset covers pre-dawn demand (biogas-fuelled, zero diesel)
8am–10am: Solar ramps up, genset shuts down at 9am automatically
10am–2pm: 2,600kW peak — BESS charging + 800kW exported to KPLC grid
2pm–8pm: Solar declining, BESS discharging — no genset required
27

## Slide 28
April: solar drops 46% — the stress month we planned for
300 MWh (April)
[chart_02_monthly_solar.html — 12-month bar chart with April highlighted amber]
April solar: 300 MWh vs July peak 510 MWh — 41% of best month
Long rains cloud cover: irradiance drops to 2.8–3.2 kWh/m²/day
Genset runs 14hr/day in April (vs 8hr dry season) — biogas-fuelled
KPLC import: ~22 MWh total year · all in April/May · cost KES 550K vs KES 16.5M export income
28

## Slide 29
Why connecting to KPLC is the correct engineering decision
KES 36M connection
Connection cost: KES 36M (4km to Matuu 33kV substation, one-time)
Returns: KES 16.5M/year net metering income + emergency April backup
Without grid: need 4× BESS (+KES 1.5B) — economically disqualifying
Thwake Dam (50km, 20MW, 2026 operational) stabilises regional grid reliability
[ Visual / Chart ]
29

## Slide 30
1,379 MWh exported × KES 12/kWh = KES 16.5M/year community income
KES 16.5M/year
Export tariff: KES 12/kWh — KPLC approved net metering rate
Annual export: 1,379 MWh — surplus after full community demand met
Annual income: KES 16.5M — single largest community revenue stream
Credits distributed pro-rata to residents via M-Pesa net metering wallet
[ Visual / Chart ]
30

## Slide 31
4,355 MWh total demand — every sector first-principles calculated
4,355 MWh
[Donut/pie chart — 10 demand sectors by MWh with percentages labelled]
Residential: 2,726 MWh (63%) · Community services: 469 MWh (11%)
Production (Jua Kali + cold storage + farm): 509 MWh (12%)
Infrastructure (boreholes + irrigation + EV): 366 MWh (8%)
Distribution losses: 323 MWh (8%) — conservative vs KPLC average 15–20%
31

## Slide 32
3,240 kWh usable beats 3,027 kWh required — 7% headroom plus genset
7% headroom
Night demand (9pm–6am): 3,027 kWh required (residential + security + borehole)
Installed: 3,600 kWh × 90% DoD = 3,240 kWh usable capacity
213 kWh headroom (7%) before Cummins C220N5 genset needs to start
Genset is third resilience layer — not primary, not secondary, but always available
[ Visual / Chart ]
32

## Slide 33
Cummins C220N5 180kW genset — 25 years reliable on biogas fuel
180 kW
Cummins C220N5 natural gas genset: 180kW rated, biogas-compatible
Dry season (July): 8hr/night baseload — covers pre-dawn demand gap
April stress month: 14hr/day — compensates for 46% solar drop
Warranty: 25,000 operating hours ≈ 25 years at this duty cycle. Zero diesel.
[ Visual / Chart ]
33

## Slide 34
2m² flat-plate per unit eliminates 1,095 MWh/year electrical demand
1,095 MWh/year
Each unit: 2m² thermosiphon flat-plate solar water heater (no electricity)
Replaces 2kW electric immersion heater × 3hr/day = 6 kWh/day/unit demand
6 kWh × 2,000 units × 365 × 70% solar fraction ÷ 3 = 1,095 MWh/year saved
Thermal solar 3× more efficient per m² than PV for hot water — correct tech choice
[ Visual / Chart ]
34

## Slide 35
Five e-matatus, 50 electric bodas, 2-minute battery swap station
2 minutes
5 × Roam Rapid e-matatus: community transport at KES 80–100 per trip
50 × Roam Air electric bodas: KES 50/day charging vs KES 200+/day petrol
Battery swap station: 1.85 kWh packs swapped in 2 minutes (Ampersand model)
EV charging demand: 269 MWh/year — fully accounted in 4,355 MWh balance
[ Visual / Chart ]
35

## Slide 36
Five numbers that close the energy case
5,734 MWh generated (solar + biogas)
KES 9/kWh community tariff
99.6% annual uptime (BESS + genset)
KES 16.5M/year net metering income
SMA Sunny Design validated April 7, 2026
vs 4,355 MWh consumed — 1,379 exported
vs KPLC KES 25/kWh — 64% cheaper
vs Yatta sub-county ~75% KPLC uptime
from 1,379 MWh export surplus
5,479.85 MWh/year — to 2 decimal places
36

## Slide 37
D
The Cognitive Community — Kenya's First
AI flood prediction · 14-node IoT sensor mesh · Swahili SMS alerts
LSTM neural network: 85–95% accuracy · 1–6 hour advance warning
BCR 61.5 — most cost-effective community safety system per person in Kenya
Already built: Red Bull Basement working prototype — hardware, not concept
37

## Slide 38
[INSERT IMAGE: Kenya flood map April 2024 / news headline collage]
Kenya 2024: 291 killed · Machakos County directly hit
291 killed
April–May 2024: worst flood season in Kenya in 30 years (national records)
291 fatalities nationally · 165,000 people displaced across affected counties
Machakos County: Yatta River and Athi River tributaries flooding sub-county roads
The 2024 extreme event is in our LSTM training data — we learned from it
38

## Slide 39
[INSERT IMAGE: Elevation cross-section showing Yatta Plateau vs Athi River floodplain]
Yatta Plateau is NOT flood-prone — this is precautionary excellence
1,450m ASL
Yatta Plateau: 1,450–1,550m ASL — well above Athi River floodplain
Machakos River floods the lowlands — Angawatch sits upland, protected
Our IoT system monitors internal drainage basin: canals, ponds, bioswales
We guard against the 1-in-50-year stormwater event on the plateau, not river floods
39

## Slide 40
We already built it — Red Bull Basement working hardware
Working prototype
Platform: ESP32 microcontrollers + LSTM neural network on Raspberry Pi
Built at Red Bull Basement programme, 2025 — functional prototype
Status: generates real Swahili SMS flood alerts from real sensor data
Hardware available for physical inspection — documented in submission Appendix C
[ Visual / Chart ]
40

## Slide 41
14 sensor nodes, one mesh — canal upstream to community boundary
14 nodes
Nodes 1–3: Yatta Canal upstream — flow rate + water level gauges
Nodes 4–6: Retention ponds — fill level + overflow trigger sensors
Nodes 7–9: Bioswale network — flow direction + accumulation sensors
Nodes 10–14: YattaFarm soil moisture + community boundary rainfall gauges
[ Visual / Chart ]
41

## Slide 42
LSTM: 85–95% accuracy, 1–6 hour advance flood warning
85–95% accurate
Long Short-Term Memory (LSTM) recurrent neural network — state of the art
Trained on 14 years Machakos County rainfall and hydrological flow data
Accuracy 85–95% validated via k-fold cross-validation on held-out data
Lead time: 1 hour minimum (fast events), 6 hours maximum (slow accumulation)
[ Visual / Chart ]
42

## Slide 43
Sluice gates open automatically — 2-second response, no human required
2 seconds
Actuated sluice gates at all retention pond outlets (motorised actuators)
LSTM triggers gate-open command automatically at WARNING threshold
2-second electrical actuation — faster than any human decision sequence
Human override available at Eco-Hub command centre — not the primary path
[ Visual / Chart ]
43

## Slide 44
Three-level Swahili alert: WATCH · WARNING · EMERGENCY
2,000 families
YELLOW WATCH: "Angalizo: mvua nyingi inatarajiwa. Hakikisha mifereji wazi."
ORANGE WARNING: "Onyo: mafuriko yanawezekana. Piga hatua za tahadhari sasa."
RED EMERGENCY: "Hatari ya dharura! Hamia eneo salama mara moja."
Three-level system prevents alert fatigue — WATCH frequent, EMERGENCY rare
[ Visual / Chart ]
44

## Slide 45
Works when grid AND cellular both fail — offline-first architecture
0 cloud dependencies
Edge inference: LSTM runs locally on each node's Raspberry Pi 4 — no cloud
BESS-backed: all sensor nodes powered from community 3,600 kWh BESS
Acoustic sirens: BESS-powered physical alert for zero-cellular scenarios
Mesh networking: nodes communicate peer-to-peer if cellular towers fail
[ Visual / Chart ]
45

## Slide 46
Same sensor mesh → precision irrigation → 21.3M litres/year saved
21.3M litres/year
Soil moisture sensors repurposed: flood detection AND irrigation control in software
Precision drip: irrigate only when soil moisture drops below calibrated threshold
Water saving vs schedule-based irrigation: 21.3M litres/year = KES 380K value
YattaFarm yield increase: 15–20% from optimal soil moisture — zero extra hardware
[ Visual / Chart ]
46

## Slide 47
Sensor data as a product — KES 425K/year from four data buyers
KES 425K/year
Pula Advisors: hyperlocal data for parametric crop insurance pricing
ACRE Africa: smallholder weather index insurance trigger calibration
Machakos County Government: early warning planning and risk assessment
KALRO: soil moisture and rainfall data for agricultural research programmes
[ Visual / Chart ]
47

## Slide 48
Eco-Hub command centre: flood + energy + farm on one screen
Dual 4K display
Dual 4K display at Eco-Hub community building, operated by cooperative committee
Left screen: live 14-node flood telemetry + LSTM prediction confidence levels
Right screen: energy production + BESS state of charge + grid export + farm data
Designed for elected community committee members — not engineers only
[ Visual / Chart ]
48

## Slide 49
KES 1.16M protects 8,090 people — BCR 61.5
BCR 61.5
Total IoT system cost: KES 1.16M (hardware + installation + year 1 communications)
People protected: 8,090 residents (entire Angawatch community)
Cost per person protected: KES 143 — cheaper than one emergency room visit
Benefit-cost ratio 61.5: every KES 1 spent generates KES 61.50 in verified benefit
[ Visual / Chart ]
49

## Slide 50
[INSERT IMAGE: Night-time aerial illustration of Angawatch community with sensor node indicator lights]
We don't just survive the climate. We master it.
Master it
14 nodes watch every raindrop before it becomes a community emergency
LSTM predicts · actuators respond · residents sleep safely — all automatic
Same sensors irrigate the farm, earn telemetry revenue, price insurance
Kenya's first community that actively learns from its own environment
50

## Slide 51
E
KES 12,213M — What It Buys Across 21 Components
Housing construction (2,000 units): KES 6,840M — the core product
Energy infrastructure (solar + BESS + biogas + genset): KES 2,100M
Site infrastructure (roads, water, sanitation, grid): KES 1,800M
Community facilities (CHC, schools, Jua Kali, Eco-Hub): KES 850M
51

## Slide 52
Six sources, one bankable capital stack — KES 12,213M total
KES 12,213M
[chart_05_capital_stack.html — Donut chart with DFI dominant at 65.8%]
DFI (AfDB/IFC/AIIB): KES 8,037M (65.8%) — construction bond, repaid by unit sales
AHP Programme: KES 1,680M (13.8%) — non-negotiable for 3BR affordability
County Bond: KES 1,000M (8.2%) · SACCO: KES 800M (6.5%)
Carbon forward KES 163M + Equity KES 532M: community and impact investor contributions
52

## Slide 53
DFI = construction finance · KMRC = take-out · Not the same shilling
Zero overlap
DFI KES 8,037M: construction bridge bond, drawn 2027–2030 during build phase
KMRC mortgages: 1,850 households × ~KES 3.5M avg = KES 6.5B over 25 years
KMRC proceeds retire the DFI bridge as each unit is sold — standard developer finance
AHP reduces price per unit independently — does not overlap with DFI or KMRC
[ Visual / Chart ]
53

## Slide 54
DTI 48.4% on 3BR — AHP subsidy is the correct policy response
48.4%
3BR EMI KES 40,803 ÷ net income KES 84,230 = 48.4% debt-to-income ratio
KMRC guideline: 40% maximum for standard approval without assistance
AHP subsidy reduces EMI by KES 5,000–8,000 → brings DTI to 42–45%
700 units × ~KES 1.5M AHP = KES 1,050M — within AHP programme parameters
[ Visual / Chart ]
54

## Slide 55
The 2BR at KES 33,015 — the sweet spot that needs no subsidy
39.2% DTI
2BR EMI KES 33,015 ÷ net income KES 84,230 = 39.2% DTI
Below KMRC 40% guideline — standard approval, no AHP subsidy required
1,130 × 2BR units: largest tier, designed specifically for KES 110K households
The product that proves the financial model without optimistic assumptions
[ Visual / Chart ]
55

## Slide 56
KES 608,968 total cash at purchase — 3.4 years saving at KES 15K/month
3.4 years
2BR total unit cost: KES 3,937,500 (VAT-inclusive at KES 46,500/m²)
10% KMRC deposit: KES 393,750
Legal fees + KMRC application + stamp duty: KES 215,218
Saving KES 15,000/month: 3.4 years to full deposit — achievable for dual-income family
[ Visual / Chart ]
56

## Slide 57
KES 182.5M per year — nine streams, zero single-point-of-failure
KES 182.5M/year
[chart_06_revenue_streams.html — Horizontal bar chart of 9 revenue streams by KES M/year]
Enterprise (Jua Kali + commercial strip): KES 92M — dominant but not monopoly
YattaFarm + chrysanthemum exports: KES 25.4M · Cooperative rentals: KES 19.8M
Grid export (net metering): KES 16.5M · E-matatu fleet: KES 13.1M
BESS grid services, CSEB, CHC, telemetry: KES 15.75M across four additional streams
57

## Slide 58
KES 79.3M net surplus — residents own the outcome
KES 79.3M/year
Revenue KES 182.5M − OPEX KES 68M − tax KES 35.2M = KES 79.3M net surplus
40%: Resident dividend — KES 1,320 per family per month via M-Pesa
30%: BESS replacement and maintenance reserve (accumulates for Year 17)
20%: Community expansion fund | 10%: County development levy
[ Visual / Chart ]
58

## Slide 59
Honest 25-year curve — Year 17 BESS replacement — breakeven Year 25
Year 25 breakeven
[chart_03_cashflow.html — Line chart cumulative position Y1 to Y25 with Y17 BESS dip]
Years 1–3: deepest deficit during construction (no revenue, full draw on DFI)
Year 5: all revenue streams active, deficit narrowing to KES 3,796M cumulative
Year 17: BESS replacement cash dip — fully funded by 30% maintenance reserve
Year 25: cumulative breakeven — community fully self-funding thereafter
59

## Slide 60
Equity IRR 12–15% — meets AfDB threshold, includes Year 17 BESS
22–28% social IRR
Equity IRR: 12–15% over 25 years (Year 17 BESS, OPEX escalation, AHP all included)
Social IRR: 22–28% (resident health gains, time savings, generational wealth)
AfDB minimum benchmark: 12% equity IRR for infrastructure — Angawatch meets it
Carbon credits (22,910 t CO₂/year Verra VCS) not in financial IRR — additional upside
[ Visual / Chart ]
60

## Slide 61
22,910 tonnes CO₂/year saved — Verra VCS registered
22,910 t CO₂/year
Solar displacing KPLC: 18,200 t CO₂/year (grid carbon factor 0.33 kgCO₂/kWh)
Biogas replacing charcoal at institutions: 2,200 t CO₂/year
EV fleet replacing petrol vehicles: 2,510 t CO₂/year
Carbon forward sale: KES 163M upfront from 10-year Verra VCS verified forward contract
[ Visual / Chart ]
61

## Slide 62
Year 5 snapshot — all systems active, net surplus positive
Year 5
All 2,000 units occupied · all 9 revenue streams fully operational
Grid export: 1,379 MWh × KES 12 = KES 16.5M (first full annual cycle)
Net surplus KES 79.3M — first resident dividend deposited via M-Pesa
BESS maintenance reserve fund begins accumulating for Year 17 replacement
[ Visual / Chart ]
62

## Slide 63
M-Pesa 2,304% return · IoT BCR 61.5 · Biogas BCR 2.8
2,304%
[chart_07_bcr_comparison.html — Log-scale BCR comparison bar chart]
M-Pesa SmartMeter: KES 2.5M investment → KES 5.76B lifetime saving (2,304% return)
IoT flood system: KES 1.16M protects KES 71.3M in assets and lives (BCR 61.5)
Biogas plant: KES 65M → KES 182M in health, cooking, and electricity benefits (BCR 2.8)
All three decisions positive · software returns eclipse hardware by orders of magnitude
63

## Slide 64
[INSERT IMAGE: Honest risk register — risks listed with specific mitigations]
Tight affordability, AHP essential — but achievable and verified
Achievable
Affordability: 3BR at 48.4% DTI — AHP is required. We designed to qualify.
Timeline: aggressive but achievable — Kenya's SGR was on-time and on-budget
Numbers: every figure third-party verified (Sunny Design, KMRC calculator, KNBS)
Risk: real but mitigated — phased build, diverse revenue, BESS maintenance reserve
64

## Slide 65
Angawatch vs Yatta Sub-County: five metrics, five wins
Energy Cost
Grid Uptime
Housing
PM2.5 (cooking)
Carbon Footprint
KES 9/kWh (Angawatch) vs KES 25/kWh (KPLC) — 64% cheaper
99.6% (Angawatch) vs ~75% (KPLC Yatta) — 24.6pp improvement
Builds equity (Angawatch) vs pays rent forever (today)
Near-zero (Angawatch) vs 300–1,000 µg/m³ charcoal (today)
22,910 t CO₂/year saved — net positive vs grid/charcoal baseline
65

## Slide 66
22,910 tonnes CO₂/year — removing 4,580 cars from Kenya's roads
4,580 cars
Solar displacing grid electricity: 18,200 t CO₂/year avoided
Biogas replacing charcoal at institutions: 2,200 t CO₂/year avoided
EV fleet replacing petrol motorcycles and matatus: 2,510 t CO₂/year avoided
Total: 22,910 t CO₂/year = equivalent to removing 4,580 passenger cars annually
[ Visual / Chart ]
66

## Slide 67
400 children breathe clean air daily — PM2.5 eliminated from institutions
400 children
[chart_08_pm25_reduction.html — Horizontal bar with WHO safe limit reference line at 15 µg/m³]
School kitchens (Phase 2 biogas): PM2.5 drops from 650 to 8 µg/m³ (98.8% reduction)
Home kitchens (Phase 1 LPG): PM2.5 drops from 650 to 20 µg/m³ (immediately, Day 1)
Community PM2.5 eliminated vs charcoal baseline: ~13.0 tonnes/year total
WHO 24-hour safe limit: 15 µg/m³ — Angawatch Phase 2 institutions: 8 µg/m³
67

## Slide 68
Cap 490 cooperative — residents vote on tariff, own the energy system
Co-op owned
Registered Cooperative Society under Cap 490 — full Kenyan cooperative law
Energy tariff voted annually by residents — any change needs 51% majority vote
All community energy assets: cooperative-owned, not private utility company
Board: 9 elected residents + 2 county nominees + 1 DFI observer (non-voting)
[ Visual / Chart ]
68

## Slide 69
One model, 47 counties — the Angawatch template is open and transferable
47 counties
Core design: CSEB + M-Pesa SmartMeter + biogas + BESS — county-agnostic
Site selection: six-variable scorecard works for any 100ha site in Kenya
Cooperative legal structure: Cap 490 applies in all 47 counties without modification
IoT mesh: same ESP32 + LSTM — retrain only the model on local rainfall data
[ Visual / Chart ]
69

## Slide 70
Four county types — four minimum adaptations, everything else identical
4 archetypes
Semi-arid (Turkana, Marsabit): larger BESS, more boreholes, less biogas feedstock
Highlands (Nyeri, Kirinyaga): smaller BESS (lower variance), possible micro-hydro supplement
Lake Basin (Kisumu, Homabay): fish cold-chain integration, lakefront orientation
Coast (Mombasa, Kilifi): seawater desalination instead of borehole, wind supplement
[ Visual / Chart ]
70

## Slide 71
47 × 2,000 = 470,000 Kenyans lifted · 1.08M tonnes CO₂/year
Families served
Residents lifted
Annual carbon saving
KMRC mortgages created
Solar installed nationally
94,000 families across all 47 counties
~470,000 Kenyans in clean-energy communities
1.08M tonnes CO₂/year at full 47-county deployment
94,000 — largest affordable housing programme in Kenya's history
157.9 MWp — equivalent to one full thermal power station
71

## Slide 72
Three asks — three critical partnerships to begin
Three asks
Ask 1: DFI partnership (AfDB / IFC / AIIB) — KES 8,037M construction finance
Ask 2: AHP qualification — non-negotiable for 3BR at KES 84,230 net income
Ask 3: Machakos County land allocation — 102ha near Matuu, Yatta Sub-County
All three asks are specific, actionable, and supported by existing government programmes
[ Visual / Chart ]
72

## Slide 73
Not a concept — a verified, prototyped, documented submission
24 sections
Red Bull Basement prototype: working ESP32 + LSTM hardware — available for inspection
SMA Sunny Design report: 5,479.85 MWh/year validated April 7, 2026 (Appendix B)
24 submission sections: every claim sourced, every number independently calculated
STS token M-Pesa SmartMeter architecture: full technical specification complete
[ Visual / Chart ]
73

## Slide 74
Angawatch. Built for Wanjiku. Powered by Kenya.
2,000 families · 8,090 residents · 102 hectares · 5,734 MWh/year
Power the Community 2026 · Energy Mentors International · April 15, 2026
gitahi.githinji@strathmore.edu · Kenya's first cognitive community
ANGAWATCH ECO-COMMUNITY
74